## Slide 1: Wireshark Tutorial
EL9333 Supplemental material for Lab 1

## Slide 2: Meet the TAs
Cing-Yu (Frank) Chu
cyc391@nyu.edu

## Slide 3: Lab Sessions
Time: Friday 4 – 6 pm, every week
Location : LC001 (B1 of the library building)

## Slide 4: About Labs
Grouping
  Labs can be done in a group of 2 people.
  Each group should only submit one copy report.
Each lab starts after the lab lecture
Deadline of each lab is before the start of the next lab
  Changes may be made to fit exam and school schedule

## Slide 5: Lab1 Objectives
Master the network measurement tool: Wireshark
Get fundamental understanding of cloud computing
Understand a typical cloud-based storage service: Dropbox & Google Drive
Observe the interactions between a Dropbox client and the cloud using Wireshark
Compare Dropbox and Google drive

## Slide 6: Wireshark
A “Packet Sniffer”: The basic tool for observing the messages exchanged between executing protocol entities.
Store and/or display the contents of the various protocol fields in these captured messages.
Passive packet sniffer: Observes packets sent and received to the machine, never sends packets by itself.
Packet Analyzer: A component of packet sniffer which displays the contents of all fields within a protocol message.

## Slide 7: Typical Packet Sniffer

## Slide 8: Download Wireshark
Visit
  https://www.wireshark.org/

## Slide 9: Start Wireshark

## Slide 10: Choose Interface

## Slide 11: Captured Packets

## Slide 12: Follow a TCP Stream

## Slide 13: Certain TCP Stream

## Slide 14: Filters

## Slide 15: Filters
Wireshark uses display filters for general packet filtering while viewing packets.
Examples:
Show only traffic in the LAN (192.168.x.x), between workstations and servers -- no Internet:
ip.src==192.168.0.0/16 and ip.dst==192.168.0.0/16
Filter out any traffic to or from 10.43.54.65:
ip.addr != 10.43.54.65
Follow a UDP Flow:
(ip.addr eq 192.168.1.15 and ip.addr eq 192.168.1.9) and (udp.port eq 58445 and udp.port eq 52068)
More info on: http://wiki.wireshark.org/DisplayFilters

## Slide 16: Wireshark sniffing (Table 1)

## Slide 17: Capture Dropbox Operations (Table 2)
Dropbox client
sniffing

## Slide 18: Capture Dropbox Operations (Table 2)

## Slide 19: Dropbox and GoogleDrive Comparison (Table 3)
computer A
computer B
subnet 1
subnet 2
T1 (start)
T2 (end)
File Size:
1 MB
10MB
100MB
(use text file)

## Slide 20: Dropbox and GoogleDrive Comparison (Table 3)

## Slide 21: Dropbox and GoogleDrive Comparison (Table 4)
File-c (100MB)
File-c copy (100MB)
sync-ed
new
how many bytes transferred?

## Slide 22: Dropbox and GoogleDrive Comparison (Table 4)